GOLDSMITH GULCH/HARVARD GULCH FLOOD WARNING PLAN

TABLE OF CONTENTS

I.	INTRODUCTION	I-1

II.	THE DRAINAGE BASIN	II-1

Drainage Basin Description	II-1

Existing flood control facilities	II-3

Flood History	II-4

Flood Hydrology	II-5

Flooding Extent (100-Year Floodplain)	II-8

III.	DECISION AIDS	III-1

General	III-1

The Decision Making Process	III-4

IV.	REQUIRED ELEMENTS OF THE WARNING PLAN	IV-1

Detection and Evaluation of the Flood Threat	IV-1

Dissemination of Warnings, Watches and Advisories to the Public	IV-2

Response of the Public to the Warning	IV-5

V.	COMMUNICATIONS	V-1

VI.	METEOROLOGICAL SUPPORT	VI-1

VII.	FLOOD THREAT RECOGNITION AND WARNING PROCESS	VII-1

Detection and Evaluation of the Flood Threat	VII-1

Dissemination of the Warning	VII-2

Step by Step Procedure	VII-2

VIII.	PROCEDURES AND GENERAL RESPONSIBILITIES	VIII-1

National Weather Service and Private Meteorological Service	VIII-1

IX.	PUBLIC DISSEMINATION	IX-1

X.	MEDIA CONTACTS	X-1

XI.	ANNUAL REVISIONS AND PRACTICES	XI-1

GOLDSMITH GULCH/HARVARD GULCH FLOOD WARNING PLAN

LIST OF FIGURES

Figure II-1	Goldsmith/Harvard Gulch Watershed	II-2

Figure II-2	Goldsmith Gulch Flooding Problem Areas	II-10

Figure III-1	100-Year Floodplain Boundary and Flood Hazard Areas	III-3

Figure III-2	ALERT Flood Detection Network	III-5

Figure III-3	Hydrologic Forecast Point Guidance	III-7

Figure III-4	Typical ALERT Stream Gage Graphics	III-16

Figure V-1	Internal Communications Flow Chart	V-3

LIST OF TABLES

Table II-1	Historic Flooding/High Water Measurements	II-5

Table II-2	1-Hour Rainfall Depths	II-5

Table II-3	Goldsmith Gulch Flood Discharges (cfs)	II-7

Table II-4	Harvard Gulch Flood Discharges (cfs)	II-7

Table III-1	ALERT Flood Detection Network	III-6

Table III-2	Urban Flash Flood Guidance	III-6

Table III-3	Convective Storm Characteristics (All depths in inches)	III-6

Table III-4	Hydrologic Forecast Point Location Descriptions	III-8

LIST OF NOMOGRAPHS

Nomograph III-1	HFP No. 1 - Harvard Gulch at Logan Street (ID 603)	III-9

Nomograph III-2	HFP No. 2 - Harvard Gulch at Harvard Avenue	III-10

Nomograph III-3	HFP No. 3 - Harvard Gulch at Race Street	III-11

Nomograph III-4	HFP No. 4 - Harvard Gulch at Jackson Street (ID 613)	III-12

Nomograph III-5	HFP No. 5 - Goldsmith Gulch at Iliff Avenue	III-13

Nomograph III-6	NFP No. 6 - Goldsmith Gulch at Eastman Avenue (ID 643)	III-14

Nomograph III-7	HFP No. 7 - Goldsmith Gulch at Union Avenue	III-15

# INTRODUCTION

This flood warning plan for the Goldsmith Gulch and Harvard Gulch drainage basins is viewed as an annex or appendix to Denver's emergency operations plan.  As such, it provides a set of operational procedures to be carried out during a flood on Goldsmith Gulch or Harvard Gulch.  The significant flood hazard areas within the two drainage basins are located within Denver, although upper portions of the two basins are located in other jurisdictions.  Therefore, planning and emergency response functions set forth in this plan are primarily allocated to Denver.

The Goldsmith Gulch/Harvard Gulch Flood Warning Plan is designed primarily to reduce the potential for loss of life resulting from flash floods on the two gulches.  This plan has been prepared by Urban Drainage and Flood Control District (UDFCD) and Denver in cooperation with the National Weather Service.  UDFCD acknowledges the valuable contributions of many individuals that assisted in preparing this plan.

Users of this plan should be aware of the area-wide meteorological support services provided through UDFCD's Flash Flood Prediction Program; the weather and flood forecast information available via the Internet, fax and email communications; and the real-time rainfall and stream level data from the automated flood detection network known as the ALERT System.

Plan holders should read the entire plan carefully to be aware of all of its elements.  Users should also understand the following:

The local governments participating in this flood warning plan believe that the early flood detection system described herein is a key component of the complete flood warning system.  They recognize, however, that the possibility of inadvertent error in design or failure of equipment to function may prevent the system from operating perfectly at all times.  Therefore, nothing contained herein may be construed as a guarantee of the system or its operation, or create any liability on the part of any party or its directors, officers, employees or agents for any damage that may be alleged to result from either operating or failing to operate the detection system or any of its component parts.
NOTE: Similar language found in Agreement No. 89-05.12

# THE DRAINAGE BASIN

This section provides an overview of the watersheds and flood hazards associated with Goldsmith and Harvard Gulch including descriptions of the drainage basin, historic floods, flood hydrology and flooding extents.  Much of the information in this warning plan was excerpted from the following flood studies:

- Urban Drainage and Flood Control District, City and County of Denver, City of Greenwood Village, Arapahoe County, Flood Hazard Area Delineation, Goldsmith Gulch and Tributaries, prepared by Gingery Associates, Inc., June 1976.

- Urban Drainage and Flood Control District, City of Greenwood Village, Arapahoe County, Flood Hazard Area Delineation, Upper Goldsmith Gulch, prepared by Moser & associates, Inc., April 2005.

- Urban Drainage and Flood Control District, Goldsmith Gulch Conditional Letter of Map Revision,  prepared by Sellard & Grigg, Inc., December 1994

- FEMA, Digital Flood Insurance Rate Map (FIRM) and Flood Insurance Study, August 16, 1995.

## Drainage Basin Description

### Goldsmith gulch

The Goldsmith Gulch watershed is a long, relatively narrow, 7.8 square mile (4936 acre) basin located in the southeast Denver metropolitan area within the jurisdictions of Denver, Greenwood Village and Arapahoe County.  The gulch is approximately eight miles in length, running from near the intersection of Arapahoe Road and I-25 to Cherry Creek near Monaco Parkway at Cook Park (Figure II-1).  The urbanized basin contains a mixture of residential and commercial uses.  There are also several major parks in the basin.

Within Denver the gulch flows through five Denver parks where the flood carrying capacity is generally adequate.  However, there are other channel reaches where channel capacity has been severely restricted, including the area between Evans Avenue and Iliff Avenue where a box culvert of limited capacity has been installed.  Urbanization has also encroached significantly on the channel between Mexico Avenue and Jewell Avenue.  There are no residential or business structures in the 100-year floodplain between Hampden Avenue and Belleview Avenue, although several road crossings in this reach do not have 100-year capacity.

### Harvard gulch

The Harvard Gulch drainage basin flows from east to west through the southern part of the City and County of Denver to the South Platte River (Figure II-1).  The total area of the basin is about 7.7 square miles (4700 acres).  Dry Gulch, with a basin area of 1.8 square miles (1150 acres) joins Harvard Gulch near Logan Street at Harvard Gulch Park.  The developed basin includes mixture of residential and commercial uses.

The original Harvard Gulch channel has been obliterated by development between the South Platte River and Logan Street, and from just west of Colorado Blvd. all the way east to the top of the basin.  The drainage system is very adequate for the more frequent heavy rain events due to a flood control project constructed in 1964.  However, there are a large number of residential and commercial structures in the 100-year floodplain.

Figure II-1	Goldsmith/Harvard Gulch Watershed

## Existing flood control facilities

### Goldsmith Gulch

There are several small detention facilities located on the gulch and its tributaries upstream (south) of Belleview.  These facilities provide some degree of flood protection in their immediate vicinity but have little effect on stream flows in Denver.  A major detention facility, consisting of two ponds known collectively as Temple Pond, has been constructed in George Wallace Park at the Denver Tech Center.  One of the ponds is formed by the I-225 on-ramp at Tamarac.  The Temple Drive embankment forms the other pond.  Various channel enlargement projects have been constructed by public and private entities over the years between Eastman Avenue and I-225.  Significant additional flood detention is provided in Southmoore Park on a tributary to the gulch.  These facilities, acting in combination with Temple Pond, provide flood protection up to the 100-year flood south of Eastman, although the 10-year flood would inundate Princeton and Kenyon Avenues and the parking lot at Tiffany Plaza.

A 100-year capacity crossing has been constructed under Dartmouth Avenue and the High Line Canal where flows enter Bible Park.  Detention has been incorporated into Bible Park to reduce downstream flows.  A 100-year crossing at Yale Avenue leads to a 100-year capacity channel between Yale and Iliff Avenues.  Additional side channel detention has been excavated immediately south of Iliff and west of the gulch.

### Harvard Gulch

In 1964, the City and County of Denver constructed a major flood control project on Harvard Gulch.  The major elements of the project include: 1) a box culvert between the South Platte River and Logan Street (Harvard Gulch Park) under Wesley Avenue, 2) a side channel detention pond in Harvard Gulch Park, 3) a second box culvert between the park at Ogden Street and Downing Street, and 4) concrete and grass-lined channels from Downing to Colorado Blvd.  Above (east of) Colorado Blvd. the channel has been obliterated and the only drainage facilities are storm sewers.

The facilities are very efficient up to their design capacity, which is less than a 10-year frequency flood.  Floods exceeding the facilities' capacity will spread out and cover a large area.

## Flood History

Little information is available on past flooding on Goldsmith Gulch. Discharge measurements, high water marks, and other flood data are limited. Historically floods have and will continue to occur in the basin.

1973, May 5-6.  A large storm causing heavy rainfall and local flooding along the mainstem of Goldsmith Gulch occurred on May 5 and 6, 1973. The estimated flood frequency resulting from this long duration storm was approximately 5-year to 10-year (Storm of May 5-6, 1973 in the Denver Metro Area: Frequency and Effect, Ducret and Hansen, USGS and UDFCD, 1973).

1991, May 23.  A hailstorm with heavy rain occurred in Arapahoe County near Goldsmith and Harvard Gulch in the afternoon between 2:00 pm and 3:00 pm.  A total of 1.75 inches of rain fell causing increased runoff and localized flooding in both Goldsmith and Harvard Gulch.

2000, July 16.  Strong thunderstorms developed approximately 5 miles west of Arvada between 7:30 pm and 9:00 pm. Very moist and unstable conditions, combined with upslope during the late afternoon and evening hours, triggered widespread urban and small stream flooding in and around the Denver metropolitan and Arvada area. Rainfall amounts generally ranged from 1 to 3 inches, with the heaviest rainfall occurring during the evening hours. Two miles east of White Ranch, an automated rain gage measured nearly 4 inches of rain (3.86 in). Since the rain fell in a relatively open area, no flood damage was reported. In Greenwood Village however, near Peoria and Bellview, the road was closed for several hours as 2 feet of standing water covered the roadway.

2001, July 8.  Up to 4.5 inches of rain fell across portions of western Arapahoe County. The underpass of Interstate 25 and Parker Road was inundated with 5 feet of water. Several other streets and underpasses in Aurora were also closed due to the high water. Heavy rain caused extensive damage to several exhibits on display at the Cherry Creek Arts Festival.

2001, July 13.  Three inches of rain reportedly fell near the Greenwood Village Police Department in a span of 15 minutes. Heavy runoff caused Toll Gate Creek to jump its banks, flooding low lying areas of Parker Road.

2003, July 19. Heavy thunderstorms caused flash flooding across parts of  western Arapahoe and southern Denver Counties. Automated rain gages indicated 2 to 3 inches of rain fell in less than one hour. The heavy runoff caused many intersections and underpasses to flood, stranding motorists. As a result, sections of Interstate 25 and Interstate 225 were closed.

2004, August 18.  Several intersections in southern Aurora were impassable due to flood waters. Two feet of water covered portions of the roadway near Park Meadows Mall. One person had to be rescued near the intersection of Arapahoe Road and Liverpool.

2005, June 3.  Thunderstorms brought heavy rain to parts of Arapahoe County. Up to 3 feet of standing water was reported over East Orchard Road. Several motorists were stranded in their vehicles and needed to be rescued.

2006, August 1.  High water inundated Arapahoe Road between Holly and Quebec. Flooding of Park Meadows Mall and areas of Greenwood Village was reported.

Table II-1	Historic Flooding/High Water Measurements

| Station | ALERT ID | Peak Stage (ft) | Peak Flow (cfs) | Date |
| --- | --- | --- | --- | --- |
| Harvard Gulch Park | 603 | 28.1 | 2,080 | July 8, 2001 |
| Harvard Gulch at Jackson | 613 | 13.9 | 990 | May 23, 1991 |
| Temple Pond | 633 | 66.9 | 640 | July 8, 2001 |
| Goldsmith Gulch at Eastman | 643 | 85.9 | 2,040 | July 28, 1997 |
| Goldsmith Gulch at Iliff Pond | 653 | 8.5 | N.A. | June 3, 2005 |
| Iliff Pond | 654 | 6.1 | N.A. | June 3, 2005 |

## Flood Hydrology

It is important to remember that many different combinations of rainfall and runoff are possible.  The information presented herein is considered reasonable for planning purposes, but is not intended as the only rainfall/runoff scenario possible.

### Rainfall

The one-hour rainfall depths for the 2-, 5-, 10-, 25-, 50-, 100-, and 500-year storm events were obtained from the UDFCD 1-hour rainfall maps.  These values were used in the modeling effort to determine discharge.

Table II-2	1-Hour Rainfall Depths

| Storm | 2-Year | 5-Year | 10-Year | 25-Year | 50-Year | 100-Year | 500-Year |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Precipitation (in) | 0.96 | 1.34 | 1.55 | 2.00 | 2.25 | 2.58 | 3.22 |

### Goldsmith Gulch

The most recent hydrologic analyses for Goldsmith Gulch include:

Flood Hazard Area Delineation for Goldsmith Gulch and Tributaries, Gingery Associates Inc., June 1976,

Goldsmith Gulch Conditional Letter of Map Revision, Sellard & Grigg, Inc., December 1994, and

Flood Hazard Area Delineation for Upper Goldsmith Gulch, Moser & associates Engineering Inc., April 2005.

These studies account for the recent changes in detention facilities and determine the peak discharges for the 10-, 50-, 100- and 500-year floods at various points along the gulch. The 100-year design hydrographs at Cherry Creek, Iliff Avenue, Yale Avenue, High Line Canal, Hampden Avenue, Quincy Avenue, I-225 and Temple Pond are provided below as are the peak discharge profiles for several design floods along the Goldsmith Gulch channel.

For the purpose of this warning plan, and to facilitate rapid assessment of the flood hazard potential of forecast or measured rainfall, decision aids have been developed for three Hydrologic Forecast Points (HFPs) on Goldsmith Gulch.  They are as follows: HFP Iliff, HFP Eastman (Stage Gage #643), and HFP Temple (Stage Gage #633).  The decision aids are contained in Section III.

### Harvard Gulch and Dry Gulch

The most recent hydrologic analysis for Harvard Gulch and Dry Gulch is contained in Flood Hazard Area Delineation, Harvard Gulch, West Harvard Gulch & Dry Gulch by Gingery Associates, Inc., dated December 1979.

The 100-year design hydrographs for Harvard Gulch at Logan Street, Downing Street and Colorado Blvd, and for Dry Gulch at its confluence with Harvard Gulch are presented as are the peak discharge profiles for the 10- and 100-year design floods along the Harvard Gulch channel.

For the purpose of this warning plan, decision aids have been developed for three Hydrologic Forecast Points (HFP) on Harvard Gulch and one on Dry Gulch to facilitate rapid assessment of the flood potential based on either forecast or measured rainfall.  They are as follows: HFP Logan, (Stage Gage #603), HFP Race, HFP Jackson (Stage Gage #613) and HFP Harvard.  The decision aids are contained in Section III.

### Flood Discharges

The discharges at select locations along the gulch for different return periods are provided below.

Table II-3	Goldsmith Gulch Flood Discharges (cfs)

|  | Return Period |
| --- | --- |
| Location | 10-Year | 50-Year | 100-Year | 500-Year |
| From 1994 Conditional Letter of Map Revision by Sellards & Grigg, Inc. |
| Confluence with Cherry Creek | 1,517 | 2,131 | 2,462 | 2,656 |
| Jewell Avenue | 1,500 | 2,002 | 2,247 | 2,533 |
| Iliff Avenue | 1,728 | 2,269 | 2,464 | 3,179 |
| Yale Avenue | 1,848 | 3,007 | 3,572 | 4,111 |
| Highline Canal | 1,759 | 2,754 | 3,224 | 3,667 |
| Southmoor Park | 1,566 | 2,355 | 2,715 | 3,067 |
| Hampden Avenue | 1,356 | 2,015 | 2,322 | 2,616 |
| Quincy Avenue | 1,144 | 1,511 | 1,621 | 1,715 |
| I-225 | 786 | 1,008 | 1,104 | 1,285 |
| Temple Pond Outflow | 887 | 1,454 | 1,690 | 1,909 |
| From 2005 FHAD Upper Goldsmith Gulch by Moser & Associates Engineering |
| Belleview Avenue |  |  | 2,555 |  |
| Prentice Avenue |  |  | 2,232 |  |
| Yosemite Street |  |  | 1,996 |  |
| Berry Avenue |  |  | 1,965 |  |
| Into Orchard Hills Park |  |  | 1,993 |  |
| West Tributary before Goldsmith Gulch |  |  | 1,006 |  |
| West Tributary Into Tommy Davis |  |  | 1,026 |  |
| West Tributary Fair Avenue |  |  | 724 |  |
| West Tributary Into Caley Detention |  |  | 883 |  |
| West Tributary Bridgewater Apartments |  |  | 381 |  |
| Goldsmith Gulch before Tributary |  |  | 886 |  |
| Into Silo Park |  |  | 1,004 |  |
| Arapahoe Lake Outfall |  |  | 787 |  |
| Arapahoe Lake SW Cove |  |  | 472 |  |
| Caley Avenue |  |  | 446 |  |
| Appletree Condos |  |  | 337 |  |
| Peakview Avenue |  |  | 244 |  |
| Arapahoe Road |  |  | 107 |  |
| Orchard Hills |  |  | 1,939 |  |
| Tommy Davis Park/Orchard Road |  |  | 965 |  |
| Caley Detention/Caley Avenue |  |  | 593 |  |
| Silo Park/Orchard Road |  |  | 756 |  |

Table II-4	Harvard Gulch Flood Discharges (cfs)

From Flood Hazard Area Delineation, Harvard Gulch, West Harvard Gulch & Dry Gulch by Gingery Associates, Inc., dated December 1979

|  | Return Period |
| --- | --- |
| Location | 10-Year | 50-Year | 100-Year | 500-Year |
| South Platte River | 3,600 | N.A. | 5,400 | N.A. |
| Logan Street | 3,400 | N.A. | 4,900 | N.A. |
| Dry Gulch | 3,400 | N.A. | 4,900 | N.A. |
| Downing Street | 2,500 | N.A. | 3,700 | N.A. |
| Race Street | 2,250 | N.A. | 3,300 | N.A. |
| Colorado Boulevard | 1,300 | N.A. | 1,900 | N.A. |

## Flooding Extent (100-Year Floodplain)

The 100-year floodplain has been delineated. The limits of the 100-year floodplain and floodway represent the area in which development is often regulated to prevent increases in water levels and increased damages during a flood. Federal and state agencies such as the Federal Emergency Management Agency (FEMA) , Urban Drainage and Flood Control District, as well as local municipalities, use the floodplain and floodway delineations as a mechanism to identify areas particularly prone to damage from flooding and to oversee development activities in these floodplains.

The basis for this floodplain and floodway delineation is the hydrology, which has been summarized in an earlier section of this report. The delineation assumes full basin development, based on land use and zoning projections provided by the affected communities, and existing channel conditions. A hydraulic analysis has been performed for the 100-year discharge, the results of which were used to plot the 100-year floodplain. Analyses were also performed for the 10-year, 50-year and 500-year discharges and are provided. The floodway has been computed for the 100-year event based on a maximum half-foot and one-foot rise in the energy grade line or water surface elevation, whichever was greater.

The U.S. Army Corps of Engineers HEC-RAS computer program was used to delineation the 100-year floodplain. The program was used to analyze the hydraulic response of the streams and floodplains using existing channel cross sections. The computational procedure used in the model is the Standard Step Method with the assumptions that the flow is steady, gradually varied, one dimensional, and slopes are relatively small. Major input parameters include digitized cross sections, roughness coefficients, channel lengths between sections, and flow rates. Bridges and culverts were simulated using surveyed field data input into the model. Flow in the channel was assumed sub-critical except near drainage structures; therefore a mixed flow regime was used to calculate the water surface elevations. Values of Manning's roughness coefficient "n" were estimated for the channel and the left and right overbanks along the channel based on field observations.

Flow through structures is sometimes partially blocked during high flood flows due to debris accumulation. Most of the structures modeled had large openings, which reduces the amount of debris caught. Based on the size of the structures, and field observations, and District approval, an area reduction coefficient was not used in the model.

The 100-year floodplain for the existing channel condition, which includes the detention capacities of various facilities, is provided. The 100-year water surface elevations and floodplain limits determined in the study represent estimates based on updated hydrology, future development, and current channel geometry in the basin. As a result, the delineation may differ from the floodplain limits identified in earlier studies.

### Description of 100-year floodPlain

This warning plan is geared toward overbank flooding from the main channel.  The user should be aware that intense rainfall can overwhelm the local storm drainage system and cause minor flooding outside any identified flood hazard area.  One such location, for example, is the intersection of Evans and Monaco in the Goldsmith Gulch basin.  Although this intersection is within the floodplain, it has experienced numerous occasions where localized rainfall caused flooding while the gulch remained well within its banks.

The approximate outlines of the 100-year floodplains are presented in this report.  Brochures prepared from these maps are distributed annually by the Urban Drainage and Flood Control District to addresses located in or immediately adjacent to the 100-year floodplains.

It should be noted that flooding of many areas will begin for floods more frequent than the 100-year flood.  Those areas are described below and are further discussed with the decision aids in Section III.

### Goldsmith Gulch Problem Areas

Flooding occurs frequently between Mexico and Evans where the channel is narrow and constrictive causing extensive flooding of surrounding properties.

The reach from Evans to Iliff Avenue includes an undersized box culvert that floods during a 10-year event.  Two houses west of Hutchinson Park and one condominium building east of the park are at risk. The undersized conduit passes between two apartment buildings and beneath parking lots for a department store and gas station. Many properties including the apartment buildings and the gas station will be inundated in a 100-year event.

From Yale to Hampden Avenue, the flood plain is contained within a well-defined channel and minimal flooding is expected. The Yale Avenue crossing overtops during a 100-year event causing Bible Park to flood upstream of Yale Avenue.

Between Hampden and I-225, the gulch passes through an improved residential green belt. The 100-year flow exceeds the capacity of the greenbelt channel and spills onto Tamarac Drive. Tamarac Drive is impassable during the 100-year event.

The crossing at Quincy Avenue is undersized to pass the 100-year event.  Approximately 23% of the estimated 100-year flow will pass over the road.

Both Belleview Avenue and Yosemite Street can pass the 100-year event.

Both the west tributary and the main tributary cross Orchard Road. The Orchard Road crossing is undersized to pass the 10-year event on both the west and main tributaries. Flooding upstream of Orchard Road will occur during a 10-year event and the roadway will become impassable.

Figure II-2	Goldsmith Gulch Flooding Problem Areas

The majority of potential damages on Goldsmith Gulch exist in the reaches below Yale where development within the 100-year flood plain has occurred and the capacity of the channel has been restricted. In this reach, all the road crossings will be overtopped and Monaco will become a carrier of floodwaters. The flood hazard not only includes the potential damage to public and private property but also involves the inability of the City to provide emergency service to th area because of the flood waters inundating the major transportation routes.

From the upstream limit of Hutchinson Park at Eastman Avenue to I-225, there are no habitable structures in the 100-year floodplain.  The bottom level of a parking structure west of the gulch and south of Eastman would be flooded during a 100-year event.  Also, the culverts under the Tiffany Square parking lot near Kenyon and Mansfield Avenues only have a 10-year capacity.

Flood response times to each Hydrologic Forecast Point (HFP) are given in Section III.

### Harvard Gulch Problem Areas

The entire drainageway from the South Platte River to Colorado Boulevard, whether in box culverts or open channels, has an approximate 10-year flood carrying capacity.  Consequently, frequent flooding is not a problem.  However, because frequent flooding does not occur, public awareness of the extent of the flood hazard is probably quite low, even with the annual map mailing described above.

Once the drainageway capacity is exceeded, the floodwaters will extend over a very wide area.  The flooding will be on the order of a couple of feet deep.  Flood response times at each HFP are given in Section III.

### Response Times

Review of the preceding information and the decision aids provided in Section III indicate a relatively short time interval between the occurrence of peak rainfall and peak runoff.  Unfortunately, this will require rapid mobilization and the potential for false warnings will be high due to the quick response time of the basin and the existing low channel capacity in several areas.

# DECISION AIDS

## General

A private meteorology service (PMS), retained by Urban Drainage and Flood Control District (UDFCD) will use decision aids for issuing appropriate messages in accordance with standard operating procedures and the supplemental information contained in this flood warning plan.  Flood conditions can be anticipated from the meteorological forecast. Measured rainfall and the site-specific decision aids and urban flash flood guidance are provided herein.  Updates to the decision aids included with this warning plan will be made as experience is gained and more data become available.

The ALERT system is an automated flood detection network consisting of self-reporting rain, stream, weather, and reservoir gages that relay data using battery-powered VHF radios.  The ALERT network in the basin consists of multiple stations that measure rainfall, stream, and reservoir information. These gages are part of a much larger network operated by UDFCD. ALERT receiving base stations located at UDFCD’s main office and the UDFCD Flood Prediction Center (FPC) collect and display data from the ALERT network in real-time.  The UDFCD base stations also host web services that allow users to view information over the Internet.  Rainfall and stream level alarms will alert users of threatening conditions.  Alarm notifications can be emailed automatically to warning plan participants.  Data from the gaging network are used to update flood peak forecasts, estimate flow arrival times and predict flood impacts at specific locations.

PMS is responsible for monitoring the FPC base station, evaluating the real-time data and updating forecasts with the use of available decision aids.  Simplified charts, tables, computer graphics and hydrologic models are the principle decision aids used to forecast flood conditions for specific problem areas.  Sections IV through VIII contain additional information concerning PMS operations and responsibilities.

Flood warning plan participants and local emergency response personnel have access to the current PMS forecast (pager, email, fax, or Internet…http://f2p2.udfcd.org).  ALERT gage data are available from Internet websites maintained by UDFCD (http://alert.udfcd.org and http://alert2.udfcd.org).  Individuals should make their own assessments of the flood threat by using the gage data, the PMS and NWS forecasts and any observations obtained from field personnel (police, sheriff, fire, public works, etc.) or other reliable sources.  Close coordination with public safety agencies should be maintained throughout this process.

The following decision aids are contained in this section of the warning plan:

- ALERT Flood Detection Network (Figure III-2).  This map shows the location of all ALERT gaging stations within the basin and in surrounding areas.

- ALERT System Summary (Table III-1).  This table provides basic information regarding each gage in the drainage basin.

- Urban Flash Flood Guidance (Table III-2).  This table provides very basic rule-of-thumb guidance to associate forecast or measured rainfall amounts with the type of flooding produced from heavy rainstorms that occur over urban areas.

- Two Hour Convective Storm Characteristics.  (Table III-3). This table is used to estimate the frequency of either forecast or measured point rainfall.  Both the total rainfall and intensity columns need to be carefully considered in making this estimate.  This table is designed for use by trained technical personnel (hydrologists and hydro-meteorologists).  In translating an estimate of precipitation frequency into a flood prediction for a specific point, the user must also estimate the spatial distribution of rain from the ALERT gages, radar, or detailed quantitative precipitation forecast (QPF); and then calculate either a total basin average or contributing drainage area relative to storm size.  Hydrologic Forecast Point (HFP) Guidance can then be used to predict flooding for specific locations.

- Hydrologic Forecast Point (HFP) Guidance.  A location map showing each HFP within the drainage basin is shown (Figure III-3) along with a description of each HFP location (Table III-4). Site-specific flash flood guidance for each HFP is provided on subsequent pages.  Certain HFPs are co-located with ALERT stream gages.  HFP decision aids can be used with either forecast or measured rainfall to anticipate flooding for known problem areas (i.e. developed floodplains, road crossings, depressions, low-lying areas, reservoirs, detention basins, etc.).

- Stage Sensor Computer Graphics.  Real-time displays of current water levels and basin rainfall have been developed for ALERT base station operations.  These displays update automatically as data are received.  Each graphics template provides information regarding local problem areas, historic floods, flood frequency data, alarm levels, elevation data and structure dimensions.

Figure III-1	100-Year Floodplain Boundary and Flood Hazard Areas

## The Decision Making Process

The earliest indication of a potential problem will likely be the forecast from PMS or NWS.  When the threat of heavy rainfall exists, PMS will provide a Quantitative Precipitation Forecast (QPF) that estimates probabilities for various precipitation amounts and identifies where the greater amounts of precipitation are most likely to occur. Table III-2 should be used to estimate the flood potential and decision-makers should consider the recommended actions. Table III-3 and the HFP decision aids (Table III-4) should than be checked to determine if the forecast rainfall will cause problems at or near the HFPs.  If no problems are anticipated based on this review, a normal level of vigilance should be maintained.  However, if the decision aids indicate a dangerous flood potential, a higher level of awareness should be maintained.

Decision makers should re-analyze flood threat once rainfall has begun and the gages are reporting.  To generate a flood projection, determine the maximum 10-, 30- and 60-minute rainfall amounts that have occurred or are projected based on measured rainfall and other meteorological information (radar, satellite imagery, upper air soundings, surface weather data, etc.).  Continue to make projections until the rainfall event has passed, problems have occurred, or the threat no longer exists.

The final confirmation that the drainage basin is indeed responding to significant rainfall is the rising stage measured by the ALERT stream gages and field reports from police, fire, public works personnel, or other reliable sources.  Although it is tempting to wait for this final confirmation, doing so will severely limit the time available to warn floodplain occupants and dispatch emergency personnel to critical areas.

It is imperative to implement the warning and response elements of this plan once a significant flood hazard exists.

Figure III-2	ALERT Flood Detection Network

Table III-1	ALERT Flood Detection Network

| ID | Station Name | Install Date | Elev (ft) | Location (Lat./Long.) |
| --- | --- | --- | --- | --- |
| 600 | Harvard Gulch Park (Precip/Stage) | 1989/07/25 | 5,315 | 39:40:20 N 104:58:56 W |
| 610 | Harvard Gulch @ Jackson (Precip/Stage) | 1989/07/25 | 5,410 | 39:40:09 N 104:56:33 W |
| 620 | Quincy/Highline (Precip) | 1989/09/19 | 5,490 | 39:38:20 N 104:56:09 W |
| 630 | Temple Pond (Precip/Stage) | 1987/05/29 | 5,575 | 39:37:55 N 104:53:28 W |
| 640 | Goldsmith @ Eastman (Precip/Stage) | 1989/09/06 | 5,480 | 39:39:22 N 104:54:08 W |
| 650 | Iliff Pond (Precip/Stage) | 2004/08/25 | 5,440 | 39:40:26 N 104:54:40 W |

Table III-2	Urban Flash Flood Guidance

| FORECAST RAINFALL | FLOOD POTENTIAL | RECOMMENDED ACTIONS |
| --- | --- | --- |
| Total amount between 0.5” to 1.0” | Streets, low-lying areas, intersections | Prepare for routine nuisance flooding |
| Total amount = 1.0” to 2.0” | All of the above plus small streams will run bankfull | Prepare for flooding of frequent problem areas |
| Total amount = 2.0” to 3.0” | All of the above plus floodplain inundation | Prepare for street closures |
| Total amount more than 3.0” | Major overbank flooding expected | Prepare for floodplain evacuations |
| Note: Rainfall amounts and guidance information apply to short duration storms (<= 1-hour) | Note: Refer to basin flood warning plans for site specific data | Note: use judgment on when to warn public, maintain contact with meteorologist |

Table III-3	Convective Storm Characteristics (All depths in inches)

| Rainfall Frequency / Probability | 10-minute Rainfall Depth | 30-minute Rainfall Depth | 1-hour Rainfall Depth | 2-hour Rainfall Depth |
| --- | --- | --- | --- | --- |
| 2-year / 50% | 0.4 | 0.8 | 1.0 | 1.2 |
| 5-year / 20% | 0.5 | 1.0 | 1.4 | 1.6 |
| 10-year / 10% | 0.6 | 1.2 | 1.6 | 1.9 |
| 25-year / 4% | 0.7 | 1.4 | 1.9 | 2.2 |
| 50-year / 2% | 0.8 | 1.6 | 2.2 | 2.6 |
| 100-year / 1% | 1.0 | 1.9 | 2.6 | 3.0 |

NOTES:

1)	For "rainfall frequency" to equal "flood frequency," the coverage of rainfall must be over the entire upstream basin.

2)	Tables III-2 and III-3 were developed to provide generalized guidance for estimating flood conditions in urban areas and for small streams draining less than 10 square miles.  Site-specific guidance should be used where appropriate.

Figure III-3	Hydrologic Forecast Point Guidance

Table III-4	Hydrologic Forecast Point Location Descriptions

| Hydrologic Forecast Point (HPF) | Description |
| --- | --- |
| HFP No. 1 | Harvard Gulch at Logan Street (ID 603) |
| HFP No. 2 | Harvard Gulch at Harvard Street |
| HFP No. 3 | Harvard Gulch at Race Street |
| HFP No. 4 | Harvard Gulch at Jackson Street (ID 613) |
| HFP No. 5 | Goldsmith Gulch at Iliff Avenue |
| HFP No. 6 | Goldsmith Gulch at Eastman Road (ID 643) |
| HFP No. 7 | Goldsmith Gulch at Temple (ID 633) |

The following pages contain site-specific flash flood guidance nomographs for each HFP.  Certain HFPs are co-located with ALERT stream gages.  The nomograph anticipates flooding for known problem areas (i.e. developed floodplains, road crossings, depressions, low-lying areas, reservoirs, detention basins, etc.) using forecast rainfall or measured rainfall. The output from the nomograph provides a decision aid to support the evaluation of flooding for critical areas.

Nomograph III-1	HFP No. 1 - Harvard Gulch at Logan Street (ID 603)

Nomograph III-2	HFP No. 2 - Harvard Gulch at Harvard Avenue

Nomograph III-3	HFP No. 3 - Harvard Gulch at Race Street

Nomograph III-4	HFP No. 4 - Harvard Gulch at Jackson Street (ID 613)

Nomograph III-5	HFP No. 5 - Goldsmith Gulch at Iliff Avenue

Nomograph III-6	NFP No. 6 - Goldsmith Gulch at Eastman Avenue (ID 643)

Nomograph III-7	HFP No. 7 - Goldsmith Gulch at Union Avenue

Figure III-4	Typical ALERT Stream Gage Graphics

Note: Graphic displays like the one above for ALERT stream gages may be viewed by clicking on flow rate or water level values on the streamflow map – http://alert2.udfcd.org/cgi-bin/gdview?tpt=map21qweb

# REQUIRED ELEMENTS OF THE WARNING PLAN

A complete flood warning plan consists of three basic elements:

1.	Detection and evaluation of the flood threat.

2.	Dissemination of the flood warnings to the public.

3.	Response of the public to the warnings.

All three parts must function properly or the warning plan will fail.  The main purpose of the warning plan is to minimize the potential for loss-of-life.  Public safety agencies will make decisions concerning floodplain evacuations and road closures.  Individuals must also make appropriate decisions to protect themselves and their families.  In some instances, a limited amount of emergency floodproofing by property owners can be accomplished.  For residences and businesses along Goldsmith Gulch and Harvard Gulch, a flash flood warning would not likely provide enough lead-time to safely effect damage prevention measures such as sandbagging.  Emergency property protection would probably be limited to turning off main gas and electricity connections.

The following pages provide a brief description of each of the three required elements listed above relative to this flood warning plan for Goldsmith Gulch and Harvard Gulch.

## Detection and Evaluation of the Flood Threat

The Goldsmith Gulch/Harvard Gulch early flood threat detection and evaluation element consists of the following items:

ORGANIZATIONS, RESOURCES AND PROCEDURES

1.	The National Weather Service (NWS) Weather Forecast Office at Boulder and their NEXRAD Doppler Radar stations located at Denver, Cheyenne and Pueblo.

2.	A private meteorological firm (PMS) retained by Urban Drainage and Flood Control District (UDFCD) to coordinate with NWS; collect and analyze all pertinent weather and flood data; prepare daily heavy precipitation outlooks; provide affected jurisdictions with early notification of flood potentials; and update jurisdictions as conditions change.

3.	The Denver Office of Emergency Management (Denver OEM) that receives and disseminates all incoming weather and flood information.  Denver OEM is the primary communications link between PMS, NWS and other flood warning plan participants.

4.	Communication arrangements defined to insure adequate communications between all parties at all times.  Primary communications are by telephone.  Amateur radio operators may be contacted to provide backup communications.

5.	Standard messages used by PMS to provide information to Denver OEM for relay to affected departments and organizations.  PMS also communicates urgent "RED FLOOD ALERT" messages directly to the Denver Wastewater Management Division (WMD) to prompt early preparedness actions on their part.

6.	An Emergency Operations Center (EOC) at Denver activated in a pre-emergency mode to gather and analyze information concerning the flood potential; maintain contacts with meteorologists, hydrologists and other support personnel; take early preparedness actions; mobilize field resources; and make warning decisions.

7.	A Flood Prediction Center (FPC) at UDFCD that is staffed by PMS when flood potentials exist.

8.	Officials from Denver who receive all critical weather and flood information and respond according to their emergency operations plan and respective internal procedures.

9.	Field personnel from police, fire, public works and other agencies dispatched to monitoring locations to report rainfall amounts, stream levels, and general flood conditions.

10.	Internal procedures and operating guidelines that are maintained, practiced and routinely updated by each participating local government agency, forecast service and support organization.

EQUIPMENT, DATA SOURCES AND DECISION GUIDANCE

1.	Satellite imagery display equipment located at NWS and PMS enabling meteorologists to see approaching weather systems and estimate local arrival times.

2.	Automated weather stations used to forecast flood potentials and predict storm development and movement.

3.	Data communications equipment, computers and software used to collect and analyze pertinent upper air and surface data.

4.	Radar product display equipment at NWS and PMS enabling meteorologists to evaluate current weather conditions; update heavy precipitation forecasts; estimate rainfall amounts at specific locations; predict storm movement, duration, and areal coverage; refine flood predictions; and anticipate specific flood problems.

5.	Automated rain and stream gages that transmit real-time data from the Goldsmith Gulch and Harvard Gulch basins to base stations located at PMS, NWS, UDFCD and Denver WMD.

6.	Decision aids that are used to quickly analyze the real-time data, refine forecasts and predict specific flood impacts.

## Dissemination of Warnings, Watches and Advisories to the Public

Several ways exist to disseminate flood warnings, watches and advisories to the public.  The delivery of public flood warnings is dependent, to a large extent, upon the electronic news media (i.e., radio and television) with NWS being primarily responsible for the initial release of the warning and its content.  Local governments are also responsible for disseminating public warning information within their political boundaries.

Three basic types of flood information are disseminated to the public:

1.	Advisory.  (meaning that nuisance flooding or flooding of a "less serious" nature is either possible or occurring);

2.	Watch.  (meaning that weather conditions are such that a hazardous flood may occur); and

3.	Warning.  (meaning that a flood that poses a significant threat to life or property is either occurring, is imminent, or has a very high probability of occurrence).

The above types of information can be issued by NWS, the local governments or both.

NWS uses the following products to convey flood information to the public and to cooperating agencies:

1.	Special Weather Statement.  This frequently issued statement may contain advisory information indicating a potential for heavy precipitation and possible flooding.  It is also used to amplify watches, warnings, and advisories by reinforcing the message, indicating what is expected, and outlining appropriate response actions.

2.	Urban/Small Stream Flood Advisory.  This advisory is typically used to indicate that minor nuisance flooding of small streams, streets, intersections and low-lying areas is imminent or occurring.

3.	Flood/Flash Flood Watch.  This product means that flooding or flash flooding is possible within the geographic area described, but that the occurrence is neither certain nor imminent.

4.	Flood/Flash Flood Warning.  This product means that hazardous flooding or flash flooding is imminent or occurring within the geographic area described.

All NWS products described above will be disseminated using NOAA Weather Radio and NOAA Weather Wire.  Flash flood watches, warnings, and urban/small stream flood advisories will also be disseminated over NAWAS.  The use of METS is limited to flash flood warnings and other warning products.

Local governments can initiate flood warnings and provide the public at risk with emergency information prior to an NWS issuance.  PMS messages, current rain and stream level data from the ALERT system, and manual field observations can be used by officials for making warning decisions (refer to Sections III and VI).  Local warnings can be disseminated over METS.  NWS will receive the information from METS and re-transmit the information as necessary and practicable.  Also, NWS can be contacted directly by local governments with additional dissemination requests.

The following presents a brief description of the several public dissemination methods mentioned in the above paragraphs along with some other available warning options:

1.	National Warning System (NAWAS).  NAWAS consists of full-period, private line voice circuits.  NWS uses NAWAS to disseminate flood advisories, flash flood watches and warnings to "Warning Points" in Colorado.  One 24-hour "Warning Point" in this system is the Jefferson County Sheriff's Department Communications Center (JCC).

2.	Metropolitan Emergency Telephone System (METS).  This is a telephone network to which government agencies and the media can subscribe.  JCC, the Jefferson County Department of Emergency Management and NWS can quickly pass information to the media subscribers for broadcast on radio and TV.  NWS uses METS for warnings, but not for watches or advisories.

3.	NOAA Weather Wire.  This is a satellite or Teletype-based communications system over which NWS can pass information to local governments or media subscribers for broadcast.

4.	NOAA Weather Radio.  This is a radio station operated by NWS (Frequencies: 162.550, 162.475, and 162.450 MHz).  Special weather radio receivers or scanners can be purchased by anyone who is interested.

5.	Emergency Alert System (EAS).  The EAS consists of radio, television, and cable outlets throughout the United States who are linked together to provide live broadcasts of  presidential messages during times of national emergency.  On a voluntary basis, the system may also be used for broadcasting state and local emergency warnings and information.  Locally, radio station KOA (850 AM) is the primary entry point for the system.  Jefferson County and NWS have input capability into the system along with the Colorado State Patrol and the Colorado Office of Emergency Management.

6.	Automated Emergency Call System.  This telephone notification method, also known as the Emergency Preparedness Network, uses the 9-1-1 Qwest phone number database to automatically dial and warn homes and businesses within affected areas concerning floods and other emergencies.  The system is capable of handling up to 1200 calls per minute.

7.	Cable Television Interrupt. This warning method is used by communications personnel to voice over-ride all cable TV programming for emergency messages.

8.	Outdoor Warning Systems.  A fixed-location outdoor siren/voice warning system in Lakewood will be used to warn people in and near the floodplain of an approaching flash flood and advise occupants to evacuate.

9.	Emergency Vehicles.  When a decision to evacuate the floodplain has been made, local law enforcement agencies and fire departments may dispatch vehicles to circulate through assigned portions of the floodplain using sirens and mobile public address systems to advise occupants to evacuate.  Standard messages to be used on the public address systems are given in Section IX.

Once the decision to warn and/or evacuate has been made, it is necessary to quickly and efficiently disseminate the warning to floodplain occupants, motorists and others at risk.  Dissemination should be made by as many different means as possible, but care should be taken to insure that warnings from different sources are similar in content.  The warning message should clearly communicate the danger and recommend specific protective actions.  For the Goldsmith Gulch and Harvard Gulch floodplains, warnings can be issued by the broadcast media, by loud speaker equipped vehicles and by fixed-location outdoor sirens.  Confirmation of the initial warning is desirable whenever possible.  People tend to seek confirmation before reacting to a warning.

All warning dissemination agencies, including the broadcast media, should have copies of the standard warning messages in Section IX.  The media must be informed beforehand of the existing hazard and the details of the warning system; and they should be checked with periodically to insure their readiness.

## Response of the Public to the Warning

If the desired response of the people in the flood hazard area to a warning is not obtained, the whole warning plan will have failed.  Cultivation of the desired response must begin well in advance of any flood threat by heightening the public awareness of the flood hazard.

These steps will be taken annually to try to cultivate the desired response:

1.	UDFCD will annually mail or deliver a brochure to all occupants of the Goldsmith Gulch and Harvard Gulch floodplains.  The brochure will contain a map of the flood hazard area and provide information on steps to take prior to flooding (plan evacuation routes, buy flood insurance, etc.) and in the event of a flood warning.

2.	Denver OEM will work with other Denver agencies (Water Department, Planning Dept., etc.) to put notices of the flood hazard in appropriate publications each spring before the flood season.

3.	Media coverage of the flood hazard, including the annual practice of the warning plan, will be sought.

# COMMUNICATIONS

Communications among personnel within participating agencies will be by normal methods now in operation.  The Denver Office of Emergency Management (Denver OEM) is the primary contact for all communications.  Denver OEM is responsible for relaying weather and flood information to other flood warning plan participants.

During emergency operations, field personnel from one agency wishing to communicate with personnel from another agency should follow their own jurisdiction's incident command system.  This will assure a system of managed communication and information flow.  If the Emergency Operations Center (EOC) is activated at Denver, the EOC will be the primary contact for all weather and flood-related communications.  The Denver OEM and EOC are collocated.

Primary communications between the National Weather Service (NWS), the private meteorological service (PMS) and Denver OEM/EOC will be by telephone.  When conditions warrant, amateur radio operators can be called into each location to establish alternate communications according to previous agreements.  Denver response agencies (police, fire, public works, etc.) will use assigned radio frequencies to communicate with field personnel.

PMS initiated communications require special emphasis.  With Denver OEM remaining the primary contact, Denver Wastewater Management Division (WMD) will also be paged directly by PMS when "Red Flood Alert" messages are issued which require priority attention on their part.  WMD will continue to receive PMS messages from Denver OEM.  Any participating entity may initiate calls to PMS or dispatch personnel to the EOC if more direct information exchange is desired.

The following page contains pertinent telephone numbers and radio frequencies.  The "Internal Communications Flow Chart" (Figure V-1) illustrates the collection and dissemination of weather information from various sources and shows the intended inter-agency flow paths for data and voice communications.

TELEPHONE NUMBERS AND RADIO FREQUENCIES

Organization	Phone Number	Frequency

*	Denver Office of Emergency Management and EOC	720-865-7600

OEM digital pager (after hours)	303-640-9999

Denver Fire Dispatch (backup for OEM)	720-913-2400

Denver Wastewater Management Division (WMD)	303-446-3400

WMD digital pager	303-640-9309

*	Arapahoe County Sheriff's Department Communications	303-795-4711

*	National Weather Service (NWS)

coordination (duty forecaster)	303-494-4479

severe weather reports	303-494-2884

administration	303-494-3210

public weather information	303-494-4221

*	Urban Drainage and Flood Control District (UDFCD)	303-455-6277

ALERT Base & Weather Bulletin Board	303-433-1247

*	Private Meteorological Service (PMS)

UDFCD Flood Prediction Center (FPC)	303-458-0789

Skyview Weather	303-688-9175

Genesis Weather Solutions	303-927-6522

Commonly Shared Emergency Radio Frequencies

CLEER "Colorado Law Enforcement Emergency Radio"	460.425

FERN  "Fire Emergency Radio Network"	154.280

NLEC  "National Law Enforcement Channel"	155.475

Other Radio Frequencies

ALERT repeaters (Blue Mountain & Smoky Hill)	171.875

ALERT gaging stations	169.525

NOAA Weather Radio (Denver)	162.550

NWR alternate 1 (Longmont/Mead)	162.475

NWR alternate 2 (Fort Collins)	162.450

Ham severe weather spotter network	146.940

alternate	147.120

Websites

ALERT System (public use)							http://alert.udfcd.org

ALERT System (public safety agency use only)				http://alert2.udfcd.org

*	Principle contact for PMS (Genesis Weather Solutions with Skyview Weather)

Figure V-1	Internal Communications Flow Chart

# METEOROLOGICAL SUPPORT

The National Weather Service (NWS) and the private meteorologist service (PMS) will provide meteorological support to Denver.  Following is the process by which NWS, PMS, and Denver should coordinate, exchange information and gear up for potential flood situations within the Goldsmith Gulch and Harvard Gulch drainage basins:

1.	NWS and PMS conduct daily weather discussions as necessary to evaluate flood potentials.  PMS will prepare daily heavy precipitation outlooks from April 15 through September 15.  This product is available from the Internet at http://alert.udfcd.org and may also be faxed to warning plan participants.  When warranted, more detailed quantitative precipitation forecasts (QPF) and storm track predictions will be issued by PMS.  Many NWS products are also available from the Internet including flood advisories, flash flood watches and flash flood warnings.

2.	When weather conditions are such that flash flood producing rains could develop, PMS will relay a MESSAGE 1 by phone to the Denver Office of Emergency Management (Denver OEM).  A MESSAGE 1 that requires priority handling will be identified as a "RED FLOOD ALERT" message.  All RED FLOOD ALERT notifications for this plan will include the Denver Wastewater Management Division as an additional contact.

3.	NWS and PMS continue their weather discussion.  If the flood potential increases one of the following actions will occur:

a.	NWS will issue a Special Weather Statement or Urban and Small Stream Flood Advisory through normal channels (NAWAS, weather wire, weather radio) and/or PMS will send a MESSAGE UPDATE to MESSAGE 1 (RED FLOOD ALERT if warranted) to Denver; or

b.	NWS will issue a Flash Flood Watch through normal channels (NAWAS, weather wire, weather radio) and PMS will send MESSAGE 2 to Denver; or

c.	PMS will send a MESSAGE 2 to Denver indicating an increase in flood potential.

4.	Observers will be designated and consideration will be given toward activating the Denver Emergency Operations Center (EOC).

5.	Regular coordination between NWS, PMS and Denver will continue.  Should the EOC be activated, PMS and NWS shall be notified immediately and regular coordination will include the EOC.

6.	When conditions warrant, NWS will issue a Flash Flood Warning through normal channels and PMS will send a MESSAGE 3 to Denver.  PMS may issue a MESSAGE 3 prior to the issuance of a NWS warning if PMS feels that a life-threatening flood is imminent.

7.	Denver will continue to monitor the situation and will begin public dissemination of warnings when necessary.  PMS will continue to send MESSAGE UPDATES as warranted.

8.	When the hazard has passed, PMS will send a MESSAGE 4 to Denver.

Throughout all of the above activities NWS and PMS will coordinate as necessary.  It must be remembered that events may occur so rapidly that it may not be possible to carry out all of the above steps.  Personnel on duty must be prepared for this possibility and must pick up the process as best they can.

The following page provides a brief description of each PMS message and their intended uses.  Subsequent pages contain the standard message forms used by Denver for documenting and relaying direct PMS communications.  These message forms should be used to insure rapid flow of information with minimum chance for error.

MESSAGE DESCRIPTIONS

MESSAGE 1 (Nuisance Flood Advisory)

This advisory message is to inform key people that weather conditions are such that nuisance flooding could develop later in the day—impacting streets, low-lying areas, normally dry gulches, small streams, and the recreational trails located along these small drainage channels.  Mud/rockslides are the primary concern for the mountains and foothills.  It will be issued by PMS after consultations with NWS.  If PMS considers the threat imminent, the message will be identified as a RED FLOOD ALERT (RFA).

MESSAGE 2 (Flash Flood Watch)

This advisory message is to inform key people that either a Flash Flood Watch has been issued by NWS or PMS believes that weather conditions are such that a life-threatening flash flood may occur later in the day.  Significant stream flooding and property damage is possible.  PMS will add any additional information that is available.

MESSAGE 3 (Flash Flood Warning)

This warning message will be issued to inform key people that a Flash Flood Warning has been issued by NWS or PMS feels that a life-threatening flash flood is imminent.  Significant stream flooding and property damage is expected.  PMS will add any additional information that is available.  This warning message should be disseminated as quickly as possible.

MESSAGE UPDATE

This message will be used by PMS to update any of the previous messages.  For example, this message can be used to narrow a watch or warning area as more information becomes available, or to provide more site-specific data and direction during an event.  If PMS considers the threat imminent, the message will be identified as an RFA.

MESSAGE 4 (All Clear)

This message cancels the flood potential status.  It is issued by PMS after consultation with NWS and other entities involved with direct PMS communications.

ABBREVIATIONS: NWS...National Weather Service     PMS...Private Meteorological Service

NOTES: F2P2 messages are used to notify local governments of potential (MESSAGE 1 and 2) and imminent (MESSAGE 3 and RFA) flood threats.  All F2P2 messages are designed for internal use and not intended for the general public.  Standard message forms are completed by the meteorologist and sent by fax or email to designated communication fan-out points prior to making contact by telephone.  Each county warning point or designated recipient follows their respective protocol for subsequent dissemination of messages.

An RFA is used when PMS believes that a nuisance flooding rainstorm is imminent and expected to primarily impact streets, low-lying areas, creek-side trails, etc.  This type of flooding is generally considered a low risk to life and property.  When a MESSAGE 2 is in effect, RFA may be used with a MESSAGE UPDATE to indicate imminent nuisance flooding that does not warrant a MESSAGE 3.  When a MESSAGE 3 is in effect, RFA may be used with a MESSAGE UPDATE when an approaching storm is expected to cause nuisance flooding outside the warning area.  Due to the short lead-time nature of the RFA, it should be disseminated as quickly as possible.

RED FLOOD ALERT:     yes     no		Received By

(circle one)		Date

Priority dissemination if yes		Time

## MESSAGE 1

(Internal Alert)

This is _____________________________________ meteorologist

(business name)	(name )

Please prepare to fill in the blanks on UDFCD/F2P2 Form M-1 concerning the possibility of flooding later today.

We have determined that the potential for flooding exists for

from 	until 	.

Prime time for flooding is from 	until 	.

(time)	(time)

The most likely areas to be impacted by flooding are (check appropriate items):

Mountain Canyon Streams & Floodplains

Urban Streams & Floodplains

Urban Streets, Intersections & Low Lying Areas

Other (describe)

The potential risk to life and property is (check appropriate item):

Low		 Moderate		 High

This message is not intended for public dissemination.  Please pass this information along to affected emergency response organizations (police, fire, public works, etc.) within your area.

Also, please take appropriate actions to prepare for possible flooding.

Further information will be provided to you as it becomes available.

AUTOMATIC RED FLOOD ALERT		Received By

Date

Priority dissemination			Time

## MESSAGE 2

(Flash Flood Watch)

This is _____________________________________ meteorologist

(business name)	(name )

Please prepare to fill in the blanks on UDFCD/F2P2 Form M-2 concerning the threat of flash flooding later today.

Use message OPTION (circle one):   A    B

OPTION A

The National Weather Service has issued a Flash Flood Watch for

which means that flash flooding is possible within the watch area.

This watch is valid from 	until 	.

(time)	(time)

We concur/disagree (circle one) with NWS watch and advises

OPTION B

We have determined that the possibility of a life-threatening flash flood exists for

from 	until 	.

(time)	(time)

Please pass this information along to affected emergency response organizations (police, fire, public works, etc.) within your area.

Also, please take appropriate actions to prepare for possible flooding.

Further information will be provided to you as it becomes available.

AUTOMATIC RED FLOOD ALERT		Received By

Date

Priority disseminATION			Time

## MESSAGE 3

(Flash Flood Warning)

This is _____________________________________ meteorologist

(business name)	(name )

Please prepare to fill in the blanks on UDFCD/F2P2 Form M-3 concerning an imminent flash flood.

Use message OPTION (circle one):   A    B

OPTION A

The National Weather Service has issued a Flash Flood Warning for

which means that flash flooding is imminent or has been reported within the warning area.

This warning is valid from 	until 	.

(time)	(time)

OPTION B

We have determined that an imminent danger of a life-threatening flash flood exists for

from 	until 	.

(time)	(time)

Please expedite this information to affected emergency response organizations (police, fire, public works, etc.) within your area.

Also, please take appropriate actions to deal with this flood threat and warn the public.

Further information will be provided to you as it becomes available.

RED FLOOD ALERT:     yes     no		Received By

(circle one)		Date

Priority dissemination if yes		Time

## MESSAGE UPDATE

This is _____________________________________ meteorologist

(business name)	(name )

Please prepare to fill in the blanks on the UDFCD/F2P2 Form M-U concerning updated information on the threat of local flooding.

This is an update to Message(s) 	 concerning possible

flooding for 	.

We advise

Please pass this information along to the emergency response organizations you have previously notified.

Also, please take appropriate action in response to the current flood potential.

Further information will be provided to you as it becomes available.

Received By

Date

Time

## MESSAGE 4

(All Clear)

This is _____________________________________ meteorologist

(business name)	(name )

Please prepare to fill in the blanks on UDFCD/F2P2 Form M-4.

The potential for flooding in

has passed.

Message Number(s) 	 are rescinded.

We will keep you advised of any changes.

Please pass this information along to the emergency response organizations you have previously notified.

# FLOOD THREAT RECOGNITION AND WARNING PROCESS

The first element of a local flood warning system is the ability to detect and evaluate a flood threat in its early stages and make the decision to warn before flood damages or deaths occur.  The second element is the dissemination of the warning to the public at risk.  The third element is the public response to the warning.  This section deals with the first two elements relative to Goldsmith Gulch and Harvard Gulch including a step-by-step illustration of how the early flood threat recognition and warning process is intended to function.

## Detection and Evaluation of the Flood Threat

The earliest recognition of a potential flood threat for Goldsmith Gulch and Harvard Gulch will be a heavy precipitation forecast by a meteorologist.  The private meteorological service (PMS) retained by Urban Drainage and Flood Control District (UDFCD) provides the meteorological support for this plan among other responsibilities.  This service supplements National Weather Service (NWS) activities by focusing its support for the six-county geographically area comprising UDFCD and tailoring communications to the individual concerns of each local government within this area.  Section VI describes the meteorological support provided by PMS and NWS.

PMS forecasts are coordinated with the NWS Weather Forecast Office at Boulder and provided to the Denver Office of Emergency Management (Denver OEM) for subsequent dissemination to affected departments including Denver's Wastewater Management Division (WMD) who has the primary overall flood management responsibility for Denver.  Participating organizations will take appropriate preparedness actions in accordance with respective internal procedures.

Five automated rain gages and four stream gages (two on Goldsmith Gulch and two on Harvard Gulch) will transmit rainfall and stream water level data to four ALERT base stations located at PMS, NWS, UDFCD and WMD.  PMS also has access to other meteorological data from weather radar, satellites, upper air soundings and weather stations.  PMS will use this data and the decision aids in Section III to predict flood potentials and update local officials concerning anticipated flood problems at specific locations.

The Emergency Operations Center (EOC) may be activated at Denver.  For flood situations, the decision to activate the Denver EOC rests with the Deputy Manager of Public Works for WMD and/or the Director of Denver OEM.  EOC personnel will have the opportunity to analyze current ALERT data, interact directly with PMS and NWS and use the decision aids provided in Section III.  EOCs may access the ALERT system via PC/phone modem connection to UDFCD's base station or from the Internet.  WMD personnel at the EOC may also assume the primary flood prediction role should communication links with PMS and NWS fail.  Denver authorities and NWS are responsible for making decisions concerning public warning.

Section VIII provides further discussion regarding procedures and general responsibilities of the principle organizations involved with this flood warning plan.

## Dissemination of the Warning

Dissemination of warning information to the public will be accomplished through the electronic media and by Denver officials.  Dissemination by the media may be channeled through NWS by local authorities or the media may be contacted directly.  NWS will use NAWAS, METS, NOAA Weather Wire, NOAA Weather Radio and/or EAS at their option to issue the public warning.  Section IV describes the various methods for disseminating flood warnings and advisories to the public.

Denver may also provide flood warnings directly to the public at risk within their jurisdiction according to internal procedures.  Standardized messages to be used by local governments are included in Section IX.

## Step by Step Procedure

The following step-by-step procedure is an idealized summary of how the flood threat evaluation and warning process is supposed to function.  THE USER MUST BE AWARE THAT THE SYSTEM WILL NOT ALWAYS FUNCTION AS PLANNED.  THE USER MUST BE PREPARED TO FUNCTION WITHIN THE FRAMEWORK OUTLINED HERE, EVEN IF ALL STEPS LISTED HEREIN DO NOT OCCUR OR OCCUR OUT OF ORDER.

A.	Normal Operations:

1.	PMS will be monitoring weather conditions on a routine basis, including appropriate coordination with NWS.  It should be noted that PMS, NWS and UDFCD have an ongoing relationship which involves forecasts of flood potential for the entire Denver/Boulder metro area; and the Goldsmith Gulch/Harvard Gulch Flood Warning Plan is an add-on responsibility for meteorologists and other technical support personnel.

2.	When weather conditions warrant, and after consultation with NWS, PMS will issue a MESSAGE 1 (messages are explained in detail in Section VI) by telephone to Denver OEM.  PMS may indicate urgency by stating that the MESSAGE 1 is a "RED FLOOD ALERT" message.  The term RED FLOOD ALERT is used to prompt priority internal message dissemination by emergency communications personnel and should not be confused with the "Red Flag Warning" fire weather product issued by NWS.  The WMD pager number will also be called by PMS when any RED FLOOD ALERT message is issued for Denver.  Section V contains details regarding weather-related communications and the flow of critical information.

3.	Denver OEM will forward the MESSAGE 1 to appropriate city and county departments and other support agencies according to internal procedures.  REMEMBER THAT A MESSAGE 1 IS A FORECAST OF A POTENTIAL FOR FLOODING.  IT IS NOT INTENDED FOR PUBLIC DISSEMINATION SIMPLY BECAUSE IT IS TOO EARLY TO TELL WHAT WILL ACTUALLY DEVELOP.

B.	Increased Awareness:

1.	PMS will continue to monitor the situation and will issue MESSAGE UPDATES (RED FLOOD ALERT if warranted) to keep local officials advised of significant changes since the previous message.

2.	NWS may issue a Special Weather Statement or other appropriate communication concerning heavy precipitation through normal channels (Section IV).  PMS may follow this with a MESSAGE UPDATE providing a more detailed interpretation of how this affects Denver and the Goldsmith Gulch and Harvard Gulch basins.

3.	Denver OEM will update key local officials concerning the increased flood potential.

4.	Contingency plans should be established to ensure that future steps in this warning plan can be carried out if needed.

C.	Flash Flood Watch:

1.	As the flood potential becomes more apparent or more threatening, NWS will issue a Flash Flood Watch for a geographic area.  The Flash Flood Watch will be issued on NAWAS, Weather Radio and Weather Wire.

2.	PMS will issue a MESSAGE 2 to Denver OEM and the WMD pager number.  MESSAGE 2 will not only indicate the issuance of a Flash Flood Watch by NWS but will also attempt to provide additional information concerning severity of the threat and a more definitive identification of areas at risk.  PMS may also issue a MESSAGE 2 without a NWS issuance of a Flash Flood Watch if PMS feels the risk is high that a life-threatening flood may occur later in the day.

3.	PMS will continue to monitor all available data and will initiate an analysis of potential flood peaks based on predicted rainfall and decision aids (Section III).

4.	As additional data (including rainfall and stream gage data) becomes available, PMS will update rainfall forecasts and flood peak projections and will provide information to Denver in the form of MESSAGE UPDATES.

5.	WMD should consider activating their EOC at this time if not done previously and maintain frequent two-way communications with PMS and NWS.

6.	Denver officials will send rain and stream observers to assigned locations.  Stream gage readings and field observations will be reported to PMS and NWS through Denver OEM or WMD.

7.	PMS will confer as needed with NWS.  When rainfall estimates or measurements, and flood peak predictions indicate an imminent flood danger; or when automated stream gages or field observations confirm the threat, a Flash Flood Warning will be issued by NWS.

D.	Flash Flood Warning:

1.	NWS will issue a Flash Flood Warning through NAWAS, METS, Weather Radio, Weather Wire and perhaps EAS.  A Flash Flood Warning means that flooding is imminent or is occurring.

2.	PMS will issue a MESSAGE 3 to Denver OEM/EOC.  PMS may also issue a MESSAGE 3 without a NWS issuance of a Flash Flood Warning if PMS feels that a life-threatening flood is imminent.

3.	Denver should then disseminate the warning within their jurisdiction according to internal procedures using standardized messages where appropriate (Section IX).

4.	PMS, NWS and stream observers will continue to monitor the situation to either confirm flooding or determine that the hazard has passed.

5.	When the threat of flooding has passed (whether a flood has occurred or not), PMS will issue a MESSAGE 4.

6.	If flooding has occurred, Denver will follow their disaster response plan.

E.	Other Considerations:

1.	As noted above, this is an idealized scenario.  It is unlikely that any flood event would be handled exactly as outlined.  Each participant must be cognizant of the probable necessity to deviate from his plan in order to react to the real situation.

2.	NWS is the only federal agency which can officially issue a Flash Flood Watch or Flash Flood Warning.  In the event of a difference of opinion between NWS and PMS, PMS will advise local officials of the difference of opinion as follows:

a.	If PMS feels a watch or warning should be issued but NWS doesn't agree, PMS will use a MESSAGE 2 or MESSAGE 3 to inform local authorities of their forecast and prompt Denver to make their own warning decision.

b.	If NWS issues a watch or warning but PMS doesn't feel it is warranted, PMS will still issue the appropriate MESSAGE 2 or 3, but indicate their misgivings.  The standard message forms in Section VI are designed to clearly indicate either concurrence or disagreement between PMS and NWS.

3.	In the event of a local decision to warn, the official in charge should immediately contact NWS to avoid public confusion.  Also, NWS may be the quickest means of notifying the public via the electronic news media.  NWS may acknowledge the involvement of local authorities (i.e., Denver, UDFCD, etc.) when issuing the warning.

4.	Flood warnings for Goldsmith Gulch and Harvard Gulch can be issued by local officials using emergency vehicle loud speakers, door-to-door notification and other methods deemed appropriate.

# PROCEDURES AND GENERAL RESPONSIBILITIES

Procedures and general responsibilities for the operational elements of this flood warning plan are contained in this section.  Three points regarding these procedures need to be emphasized:

1.	The operating procedure for each organization addresses only those actions and activities that organization must accomplish in order to effect a coordinated response to a flood situation within the Goldsmith Gulch and Harvard Gulch drainage basins.

2.	Every individual responsible for the implementation of any part of this warning plan should be familiar with the entire plan.

This section does not contain detailed operating procedures but provides an overview of technical support activities, communications, emergency operations and general responsibilities of each participating organization.  Specific task assignments and responsibilities are described in local emergency operation plans and other supplemental documents maintained by local governments.  Similarly, the technical support organizations including National Weather Service (NWS) and Urban Drainage and Flood Control District (UDFCD) and their private meteorological service (PMS) routinely update their own internal operating procedures, policies and duty manuals.

## National Weather Service and Private Meteorological Service

The NWS Weather Forecast Office at Boulder has the responsibility for issuing Flash Flood Watches, Flash Flood Warnings, general Flood Warnings, and many other types of weather warnings, advisories and forecasts for northeastern Colorado, including the City and County of Denver, in which Goldsmith Gulch and Harvard Gulch are located.  The upper portion of Goldsmith Gulch is located in Arapahoe County.  PMS has been retained by the UDFCD to supplement NWS flood-related activities within UDFCD boundaries, which includes the Goldsmith Gulch and Harvard Gulch drainage basins.  PMS is responsible for monitoring weather and flood conditions, forecasting flood potentials, issuing standardized internal messages, and directly advising local officials concerning specific flood threats.  UDFCD provides PMS with access to weather radar, satellite data, lightning data and ALERT base stations, that collect real-time rain, stream levels, and surface weather data from the Goldsmith Gulch/Harvard Gulch Flood Detection Network and other detection networks operating in or near the Denver/Boulder metropolitan area.  PMS acquires additional meteorological data, performs their own analyses and prepares forecasts tailored to local government needs.  Coordination between NWS and PMS will be as follows:

1.	Coordination between NWS and PMS will be initiated by either party when it is deemed that the potential for flash flood producing storms exists.  A private line at the Flood Prediction Center (FPC) located at UDFCD has been established for this purpose.  NWS and PMS will consult on when to issue a MESSAGE 1 (see Section VI for MESSAGE descriptions) to the Denver Office of Emergency Management (Denver OEM) or Fire Dispatch.  MESSAGE 1 will be communicated by phone and fax.  PMS personnel will establish support operations at the FPC either before or soon after a MESSAGE is issued.

2.	If PMS feels that a MESSAGE 1 requires priority handling by emergency communications personnel, the message will be preceded by the statement:  "THIS IS A RED FLOOD ALERT MESSAGE."  The RED FLOOD ALERT message should not be confused with the "Red Flag Warning" fire weather product issued by NWS.

3.	Coordination between NWS and PMS will continue at two-hour intervals or less as needed until the potential passes or a more serious situation develops.  NWS may issue a Special Weather Statement or Urban and Small Stream Flood Advisory through normal channels if conditions warrant (see Section IV for discussion of NWS products).

4.	If the situation is up-graded to a Flash Flood Watch by NWS, they will notify PMS and put the watch out on NOAA Weather Wire, NOAA Weather Radio, and NAWAS.  After being contacted by NWS, PMS will immediately issue a MESSAGE 2 to Denver and Arapahoe County.

5.	If PMS feels the flood potential has increased but NWS does not want to issue a Flash Flood Watch, PMS can either issue a MESSAGE UPDATE to affected local governments indicating an increase in flood potential or upgrade the message status to a MESSAGE 2 if they feel a life-threatening flood potential exists.

6.	Following receipt of a MESSAGE 2 or MESSAGE UPDATE, Denver should pass along any rainfall or other data available to them and inform PMS and NWS of such observations.

7.	Communications between NWS, PMS and Denver will continue as needed.

8.	If the situation is up-graded to a Flash Flood Warning by NWS, they will notify PMS and put the warning out on NOAA Weather Wire, NOAA Weather Radio, NAWAS and METS.  After being contacted by NWS, PMS will immediately issue a MESSAGE 3 to Denver and Arapahoe County.  PMS can also issue a MESSAGE 3 without a NWS Flash Flood Warning if PMS believes a life-threatening flood is imminent.

9.	PMS can issue a MESSAGE UPDATE to affected local governments at any time an update of the current message in effect is warranted but the next higher or lower message is not appropriate.

10.	Local government officials may recognize the equivalent of a Flash Flood Warning, independent of NWS or PMS, if they feel the situation warrants.  NWS and PMS should be immediately advised of this circumstance.

11.	Local government officials may decide on their own to evacuate the floodplain, close roads or take some other appropriate emergency action.  NWS and PMS will be informed of the situation immediately.  NWS will disseminate this information over their communications network wherever possible.

12.	Consultations between NWS, PMS, Denver, and other flood warning plan participants should continue as needed until the potential has passed or a flood is occurring.

13.	When NWS and PMS agree that the potential has passed, PMS should issue a MESSAGE 4 to Denver and Arapahoe County.

PMS will have forecaster(s) on duty from 7 AM until 10 PM each day.  If a potential exists at that time, PMS will remain staffed until the potential has ended.  If a flash flood potential exists at 10 PM, PMS will continue to staff the FPC until the potential has ended.  If weather conditions change after 10 PM and a potential flood situation develops, NWS will notify the PMS duty person.  This individual will respond to the FPC and begin the coordination process described above.

## City and County of Denver

The Wastewater Management Division (WMD) of Denver's Public Works Department is the primary agency responsible for initiating emergency activities relative to potential flooding on Goldsmith Gulch and Harvard Gulch.  WMD makes the decision to activate forces, including the activation of Denver's Emergency Operations Center (EOC), based on the flood potential contained in the weather forecast.  When activated, WMD begins the coordination necessary to establish the Incident Command Network for floods.  This network becomes an integral part of the Incident Command System (ICS) established at the EOC.  The Deputy Manager of WMD serves as the Incident Commander for flood emergencies.

The following pages, excerpted from Chapter 2 of Denver's Standard Operating Procedure for Floods, summarize the general responsibilities of key flood response agencies:

# PUBLIC DISSEMINATION

The first response of many people when they hear a warning is to try to confirm it from another source.  Therefore, it is very important that all public dissemination messages present the same information.  The messages in this Section are written to insure that the same information is given from all possible sources.

This Section contains two types of messages:

1.	Messages to be broadcast to the public and the media; and

2.	Messages to be used by emergency vehicles circulating through the floodplain or by existing public address systems.

The messages are written in fill-in-the-blank format.  Information to fill in the blanks will be provided by local authorities from Denver OEP or EOC, if activated.

CITIZEN ALERT MESSAGE A1

The following message may be used when the National Weather Service has issued a Flash Flood Watch:

THE NATIONAL WEATHER SERVICE HAS ISSUED A FLASH FLOOD WATCH FOR

(geographic area)

A FLASH FLOOD WATCH MEANS FLOODING IS POSSIBLE WITHIN THE WATCH AREA.  PERSONS IN THE WATCH AREA ARE ADVISED TO PREPARE FOR POSSIBILE FLASH FLOODING, KEEP INFORMED, AND BE READY FOR QUICK ACTION IF FLASH FLOODING IS OBSERVED OR A FLASH FLOOD WARNING IS ISSUED.

CITIZEN ALERT MESSAGE A2

The following message may be used if the National Weather Service has not issued a Flash Flood Watch but local government officials believe that flash flooding is possible:

PERSONNEL

(local government agency or agencies)

HAVE DETERMINED THAT A FLASH FLOOD IS POSSIBLE WITHIN

(geographic area)

PERSONS WITHIN THIS AREA ARE ADVISED TO PREPARE FOR POSSIBLE FLASH FLOODING, KEEP INFORMED, AND BE READY FOR QUICK ACTION IF FLASH FLOODING IS OBSERVED OR A FLASH FLOOD WARNING IS ISSUED.

EVACUATION MESSAGE

The following message may be used if a decision has been made to warn people in the floodplain to evacuate:

THE 	WARNS

(responsible agency)

THAT FLOODING WILL BEGIN AT 	 AT

(location)

APPROXIMATELY 	.

(estimated time)

HAS URGED EVERYONE IN THE

(person in authority)

FLOOD HAZARD AREAS TO EVACUATE THE AREA IMMEDIATELY.  PERSONS EVACUATING THE AREA SHOULD MOVE AWAY FROM THE CREEK.  DO NOT ATTEMPT TO OUT-RUN A FLOOD IN YOUR VEHICLE.  DISPLACED PERSONS SHOULD GO TO

.  (Add any confirmed reports of flooding or heavy rainfall). 	(place)

DO NOT ATTEMPT TO CROSS A FLOODED AREA ON FOOT OR IN YOUR VEHICLE.

SUPPLEMENTAL (check appropriate statements):

DO NOT ENTER BARRICADED AREAS.

ABANDON YOUR VEHICLE IMMEDIATELY WHEN WATER RISES ABOVE THE ROAD ON WHICH YOU ARE DRIVING.

IF YOU ARE DRIVING IN A MOUNTAIN CANYON, ABANDON YOUR VEHICLE IMMEDIATELY AND CLIMB TO HIGH GROUND.

EMERGENCY VEHICLE/PUBLIC ADDRESS MESSAGE

The following message may be used over public address systems or by emergency vehicles circulating in the floodplain:

THIS IS

(emergency service agency)

FLOODING WILL BEGIN AT 	 AT

(location)

APPROXIMATELY 		.

(estimated time)

HAS URGED EVERYONE IN THE FLOOD

(person in authority)

HAZARD AREAS TO EVACUATE THE AREA IMMEDIATELY.  PERSONS EVACUATING THE AREA SHOULD MOVE AWAY FROM THE CREEK.  DO NOT ATTEMPT TO OUT-RUN A FLOOD IN YOUR VEHICLE.  DISPLACED PERSONS SHOULD GO TO

.  (Add any confirmed reports of

(place)

flooding or heavy rainfall.)  DO NOT ATTEMPT TO CROSS A FLOODED AREA ON FOOT OR IN YOUR VEHICLE.

SUPPLEMENTAL (check appropriate statements):

DO NOT ENTER BARRICADED AREAS.

ABANDON YOUR VEHICLE IMMEDIATELY WHEN WATER RISES ABOVE THE ROAD ON WHICH YOU ARE DRIVING.

# MEDIA CONTACTS

Each year, prior to the flood season, the Urban Drainage and Flood Control District (UDFCD) will inform the news media of the flood hazard associated with Goldsmith Gulch, Harvard Gulch and other tributaries.  The media will be requested to publicize the hazard by providing information about this flood warning plan, including steps occupants of the hazard area should take when a flash flood warning is issued.

UDFCD will also, on an annual basis, work with local public information offices to make the broadcast media aware of how the sample advisory and warning messages contained in Section IX may be used.

# ANNUAL REVISIONS AND PRACTICES

Each year, prior to the beginning of the active flood season, the Urban Drainage and Flood Control District (UDFCD) will issue appropriate revisions to this document, after consulting with affected emergency managers and other appropriate local officials.  If no revisions are needed, UDFCD will inform plan holders, accordingly.

UDFCD will also schedule at least one annual practice exercise.  The exercise may take various forms including tabletop simulations, message dissemination/communication tests, functional exercises involving field operations, combinations of the preceding examples, or a less complex orientation meeting.  The exercise may be publicized by local public information offices or by UDFCD to further increase public awareness of the flood hazard and help attain the desired public response when flash flood warnings are issued.

# Text boxes

Leyden Lake Inflow Present Basin Conditions